## Slide 1
Date: 2023/04/26
Meeting: In-person meeting
Time: 14:40 – hh:mm JST
APRS STUDENT MISSION – Weekly meeting
JAVIER FERRER TA PHUONG LINH

## Slide 2: Component block diagram (tentative)
Ref components:
MCU
Sound card
Interface card (octocoupler)
Radio transceiver
Antennas
- Eggbeater
- Monopole
- ¼ wave ground plane monopole

## Slide 3
Eggbeater antenna
Raspberry Pi Zero (top)
and Pi 3 B (bottom)
Yaesu FTM 100-DH
Radio transceiver
WM8960 Hi-Fi Sound Card HAT
Easy DIGI Interface Card

## Slide 4: EPS block diagram (tentative)
Notes:
For the system power supply, we can use a Solar panel, which connects with a Rechargeable battery by a power charger/ controller circuit.
It is probably that the Sensors Interface block needs it own battery which does not relate to the Rechargeable battery

## Slide 5: Sensors that we are currently considering (based on type of data):
Air vibration:
  INFRASONIC SENSOR TYPE7744N (ACO CO., LTD)
  MB3a (SEISMO WAVE)
Gas sensor:
  RKI ES-1827I Replacement Sensor (PREMIERSAFETY)
  KHS-5P (Komyo Rikagaku Kogyo)
Ash sensor:
  Parsivel2 (OTT)

## Slide 6: Sensors that should be added (based on type of data):
Ground deformation (using ground-based monitoring approach):
  Using GPS data of our RF Transceiver
  Using GPS sensors
      JLR-4350 (JRC)
      Key specifications:
Accuracy: 5m (GPS); 4m (when combining GPS with other positioning systems)
Sensitivity: < -144 dBm
Position update: every 1 sec (normally)
Mass: Approx. 1.2 kg
Operating temperature: -25 ℃ to +55 ℃
Notes: Reason:
- Ground deformation occurs due to the movement of magma and other fluids in the subsurface before, throughout, and after an eruption (USGS). Thus, it ‘s very important to know this data for volcano monitoring

## Slide 7: On-going activities

## Slide 8: Volcano monitoring
Radio transceiver
(YAESU FTM-100DH)
Sensors
(types of sensors)
Microcomputer
(Raspberry Pi 3)
VHF Omni Antenna
Sensor interface board
(optional)
External sound card
(WM8960)
Interface card
(Easy digi)
SOLAR PANEL
Battery (Lead acid)
Power distribution circuit
Power recharge/ controller
Candidates:
1. Eggbeater
2. Monopole antenna
Another option

## Slide 9: Other antenna candidates
Other Monopoles
- Shakespear HA156c
- Diamond SG-7900 144/430MHz VHF UHF